## Slide 1
BRIDGE DESIGN
for Cambridge and Newcastle

## Slide 2
London
Cambridge
Cardiff
Newcastle-Upon-Tyne

## Slide 3
River Bridges - Cambridge
  River Cam
  Upper River – out of the city to the south; mainly punts, canoes.
  Middle River – through the city centre and at the college backs; mainly punts, canoes.
  Lower River – out of the city to the north; mainly rowing boats, house boats, commercial sightseeing boats.
Cambridge City
The River Cam

## Slide 4
River Bridges - Newcastle
  River Tyne.
  Much deeper and wider than the Cam.
  Bridges over the river are between Newcastle-upon-Tyne to the North and Gateshead to the South.
  Still used for industrial and commercial traffic – tankers, sailing ships, passenger cruisers.
Newcastle-upon-Tyne
Gateshead
River Tyne
to the sea

## Slide 5
Road/Rail Bridges
    Bridges aren't just over water
    Can be over railways, roads or other natural hazards such as ditches.
    Similar considerations to bridges over water.

## Slide 6
Bridge Design
In groups: What factors will affect the design of a bridge? Which of these will be different in Cambridge and Newcastle?
  Traffic – Pedestrians, Cars, Trains or Freight Lorries?
  Required Span – A bridge over the Tyne would need to be much longer than over the Cam.
  Required Clearance – would need to be much larger on the Tyne than on the Cam.
  Budget – how much have you got to spend? Most of the time the aim is to minimise cost but this may mean sacrificing on other aspects of the design.
  Timescale – how long have you got to build it?
There are many types of bridge to choose from, each of which provides a different solution to these problems.....

## Slide 7
Arch Bridges
  Arch bridges usually need firm embankments as they create large forces at their abutments.
  The Tyne bridge in Newcastle is an example of a steel arch bridge (the Tyne bridge is a special type of arch known as a tied or bowstring arch)‏
  The Fen Causeway Bridge in Cambridge is an example of a concrete arch bridge.
  There are many examples of masonry arch bridges in Cambridge, although masonry is not often used in modern bridge construction. The oldest masonry arch bridge in Cambridge is Clare College Bridge, built in 1640.
Tyne Bridge, Newcastle
Opened 1928

## Slide 8
Beam Bridges
There are many examples of Truss Bridges in Newcastle and a few in Cambridge.
  Truss bridges come in many shapes and materials, the criss-crossing members provide support to the main beams and allow longer spans.
Elizabeth Way Bridge, Cambridge is an example of a Box Girder Bridge.
  Main beams are girders in the shape of a hollow box.
  Often made of concrete or steel.
Beam bridges in their basic form are very simple
  Beam Supported on two piers
  Spans tend to be short - limited by beam stiffness
King Edward VII Bridge.
Opened 1906

## Slide 9
Cable-Stayed Bridges
Tony Carter Bridge over Cambridge railway – example of a Cable -Stayed bridge.
  Cables tie bridge deck directly to towers.
  Spans not as large as suspensions bridges, smaller towers.
  Can be in harp of fan design.
There are no examples of Suspension bridges in either Cambridge or Newcastle. This type of bridge is mainly used for very long span applications and is relatively expensive for the shorter spans likely in cities like these.
Suspension Bridge Cable Stay Bridge Cable Stay Bridge
- fan design - harp design

## Slide 10
Interest Groups
Who should be considered when designing a bridge?
Who should have a say in the design of a bridge?
Divide into groups:
Bridge Users
River Users
Local Residents
Local Council (in this case = Client)‏
What aspects of design would be important to your interest group?
Appearance, cost, length of building works, intrusion of building works?