## Slide 1
FORCES - BRIDGES
Tyne Bridge, Newcastle

## Slide 2
The Tyne Bridge, Newcastle.
  Opened in 1928.
  Design by Mott, Hay and Anderson, based on their design of the Sydney Harbour Bridge in Australia.
  When it was opened by King George V it was the longest single-span bridge in the UK.
  The engineers had to analyse the Tyne Bridge as a complete structure so that it would stand up once built but they also had to think about how to hold it up while it was being constructed...

## Slide 3
Construction
  Road ways on either side of river built to correct height.
  Used as supports for construction of arch and main bridge deck.

## Slide 4
Construction
  Each half built outwards from the bank
  During construction, incomplete sections 'tied-back' to temporary towers on the bank.

## Slide 5
Construction
  Spans joined in the middle
  Vertical ties attached then bridge deck built when arch complete.

## Slide 6
Construction Sequence
How would the forces change in the tie supports during construction?

## Slide 7
Analysis
Because the bridge is symmetrical, we can just look at one half to assess the forces in the support cable.
We can then draw a free-body diagram of this half-arch:
W
T
Rv
Rh
X
H
To simplify the analysis we can model this section as a straight line. This assumption is valid as long as we keep the distances to the pivot, H and X, the same.
pivot